| TABLE NO | 1 |  | 2 |  | 3 |  | 4 |  | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| EXAMPLE ORDER NO 502 | 006 |  | M |  | 1M |  | 010 |  | 8 |

Example Order No. =  Type 502 tapered drilled bar stock  thermowell ; 6” length ; 1/2" NPT process connection ; 1/2" NPT sensor connection ; 10” total overall length ; 316 ST.ST.

| Table 1. Dimension “U” |  | Table 2. Process Connection |  | Table 3. Sensor Connection |
| --- | --- | --- | --- | --- |
| Insert “U” in inches. ( 3 digit ) |  | Order | Diameter |  | Order | Description |
|  |  | M | 1/2“ N.P.T |  | 1M | 1/2" N.P.T |
|  |  | R | 1/2" B.S.P |  | 1R | 1/2" B.S.P |
|  |  | Q | 3/4" N.P.T |  | 1O | Other |
|  |  | V | 3/4" B.S.P |  |  |  |
|  |  | O | Other |  |  |  |
| Table 4. Dimension “A” |  | Table 5. Well Material |  |  |
| Insert “A” in inches. ( 3 digit ) |  | Order | Description |  |  |  |
|  |  | 4 | 310 ST.ST |  |  |  |
|  |  |  | 8 | 316 ST.ST |  |  |  |
|  |  |  | 9 | 304 ST.ST |  |  |  |
|  |  |  | 10 | Other |  |  |  |

NOTES :

- “D” and “d” are propotional to the process connection :

For 1/2"  D=18 mm  d=15 mm.

3/4"  D=23 mm  d=18 mm.

1"  D=29 mm  d=18 mm.

- Standard Length,  “A” = “U” + 44mm.

- For extension type,   “A” = “U” + “T”  + 44 mm.

# Text boxes

Type 502 is a heavy duty tapered drilled bar stock thermowell, protecting heavy industry application sensors from corrosion, high pressure and high velocity elements.

Type 502 is available in

a variety of features and options to meet users' specific requirements, including:

- Immersion Length

- Process Connection

- Sensor Connection

- Overall Length

- Well Material

TYPE 502

## HOW TO ORDER