| TABLE NO | 1 |  | 2 |  | 3 |  | 4 |  | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| EXAMPLE ORDER NO 503 | 006 |  | M |  | 1M |  | 012 |  | 8 |

Example Order No. =  Type 503 stepped  bar  stock  thermowell ; 6” length ;

1/2" NPT process connection ; 1/2" NPT sensor connection ; 12” overall length ; 316 ST.ST.

| Table 1. Dimension “U” |  | Table 2. Process Connection |  | Table 3. Sensor Connection |
| --- | --- | --- | --- | --- |
| Insert “U” in inches. ( 3 digit ) |  | Order | Diameter |  | Order | Description |
|  |  | M | 1/2“ N.P.T |  | 1M | 1/2" N.P.T |
|  |  | R | 1/2" B.S.P |  | 1R | 1/2" B.S.P |
|  |  | Q | 3/4" N.P.T |  | 1O | Other |
|  |  | V | 3/4" B.S.P |  |  |  |
|  |  | O | Other |  |  |  |
| Table 4. Dimension “A” |  | Table 5. Well Material |  |  |
| Insert “A” in inches. ( 3 digit ) |  | Order | Description |  |  |  |
|  |  | 4 | 310 ST.ST |  |  |  |
|  |  |  | 8 | 316 ST.ST |  |  |  |
|  |  |  | 9 | 304 ST.ST |  |  |  |
|  |  |  | 10 | Other |  |  |  |

NOTES :

- “D” and “d” are propotional to the process connection :

For 1/2"  D=18 mm  d=15 mm.

3/4"  D=23 mm  d=18 mm.

1"  D=29 mm  d=18 mm.

- Standard Length,  “A” = “U” + 44mm.

- For extension type,   “A” = “U” + “T”  + 44 mm.

# Text boxes

Type 503 is a heavy duty stepped drilled bar stock thermowell for use under critical conditions, such as high temperature and high pressure, ensuring a long service life and accurate measurement of your process.

This thermowell is used in heavy industry, such as power plants, oil refineries, chemical and petrochemical plants.

Type 503 is available in

a variety of features and options to meet users' specific requirements, including:

- Immersion Length

- Process Connection

- Sensor Connection

- Overall Length

- Well Material

TYPE 503

## HOW TO ORDER