| TABLE NO | 1 |  | 2 |  | 3 |  | 4 |  | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| EXAMPLE ORDER NO 506 | 014 |  | 1” ASA 150 |  | 1M |  | 016 |  | 8 |

Example Order No. =  Type  506  flanged stepped drilled thermowell ;

14” immersion length ; 1” ASA 150 flange connection ; 1/2” NPT sensor connection ; 16” overall  length ; 316 ST.ST.

| Table 1. Dimension “U” |  | Table 2. Process Connection |  | Table 3. Sensor Connection |
| --- | --- | --- | --- | --- |
| Insert “U” in inches. ( 3 digit ) |  | Indicate flange details as per ASA Type |  | Order | Description |
|  |  |  |  | 1M | 1/2" N.P.T |
|  |  |  |  |  | 1R | 1/2" B.S.P |
|  |  |  |  |  | 1O | Other |
| Table 4. Dimension “A” |  | Table 5. Well Material |  |  |
| Insert “A” in inches. ( 3 digit ) |  | Order | Description |  |  |  |
|  |  | 4 | 310 ST.ST |  |  |  |
|  |  |  | 8 | 316 ST.ST |  |  |  |
|  |  |  | 9 | 304 ST.ST |  |  |  |
|  |  |  | 10 | Other |  |  |  |

NOTE :

- “D” and “d” are  proportional to the process connection.

For Flange <= 1” ASA  150   “D”=18 mm   “d”=15 mm.

For Flange  >  1” ASA  150   “D”=23 mm   “d”=18 mm.

# Text boxes

Type 506 is a heavy duty stepped drilled bar stock flanged thermowell for use under critical conditions, such as high temperature and high pressure, ensuring a long service life and accurate measurement of your process.

This thermowell is used in heavy industry, such as power plants, oil refineries, chemical and petrochemical plants.

Type 506 is available in a variety of features and options to meet users' specific requirements, including:

- Immersion Length

- Process Connection

- Sensor Connection

- Overall Length

- Well Material

TYPE 506

## HOW TO ORDER